## Slide 1: CHEVY CHASE DRIVE LANE REDUCTION STUDY
Community Outreach Meeting
March 22, 2017
6:30 PM

## Slide 3
  PURPOSE OF STUDY
To Evaluate the Feasibility of Reducing Chevy Chase Drive from 4 Travel Lanes to 2 Travel Lanes with a Continuous Two-Way Left-Turn Lane and 2 Bicycle Lanes

## Slide 4: CHEVY CHASE DRIVE REDESIGN LANE REDUCTION
Existing Lane Reduction Test Case

## Slide 5: SCOPE OF STUDY
Conduct Vehicle, Pedestrian and Bicycle Volume Counts
Review Collision Records Involved Unsafe Speed, Pedestrians and Bicyclists
Conduct Speed Survey
Calculate Intersection Level of Service and Average Delay
Conduct Travel Time Study
Computer Model Simulation (SimTraffic)

## Slide 6: VEHICLE VOLUMES
Vehicle Count AM & PM Peak Hour
February 5, 2014

## Slide 7: BICYCLE VOLUMES
Bicycle Count AM & PM Peak Hour
February 5, 2014

## Slide 8: Collision Involved: Unsafe Speed
From 1/1/2011 to 12/31/2015
Total Collisions: 11
E Chevy Chase Drive
Boynton Street
S Glendale Avenue
S Chevy Chase Drive
S Adams Street

## Slide 9
Collision Involved: Pedestrians
From 1/1/2011 to 12/31/2015
Total Collisions: 5
Glendale Avenue
E Chevy Chase Drive
Brand Boulevard

## Slide 10
Collision Involved: Bicycles
From 1/1/2011 to 12/31/2015
Total Collisions: 4
E Chevy Chase Drive
Boynton Street
S Chevy Chase Drive
S Adams Street

## Slide 11: SPEED SURVEY
Chevy Chase Drive between Boynton Street and Adams Street
  Speed Limit = 35 MPH
  Average Speed = 29 MPH
  85th Percentile Speed = 37 MPH

## Slide 12: INTERSECTION LEVEL OF SERVICE
AM Peak Hour Intersection Level of Service |  |  |  |  | 
Intersection | Control | Avg. Delay w/o Lane reduction (sec/veh) | LOS | Avg. Delay w. Lane reduction (sec/veh) | LOS
Chevy Chase/Glendale | Signalized | 33.5 | C | 34.1 | C
Chevy Chase/Mariposa | SSSC | 28.1 | D | 19.9 | C
Chevy Chase/Boynton | Signalized | 13.4 | B | 26.2 | C
Chevy Chase/La Boice | SSSC | 10.4 | B | 18.0 | C
Chevy Chase/Adams | Signalized | 13.7 | B | 18.8 | B
Chevy Chase/Tyler/Acacia | Signalized | 69.9 | E | 77.5 | E
Notes: For signalized intersections, average intersection delay is reported in seconds per vehicle for all approaches. For side-street stop-controlled intersections, the delay and LOS for the most delayed individual movement is shown. All results are rounded to the nearest second. Source: Fehr & Peers, 2014 |  |  |  |  | 

## Slide 13: INTERSECTION LEVEL OF SERVICE
PM Peak Hour Intersection Level of Service |  |  |  |  | 
Intersection | Control | Avg. Delay w/o Lane reduction (sec/veh) | LOS | Avg. Delay w. Lane reduction (sec/veh) | LOS
Chevy Chase/Glendale | Signalized | 32.4 | C | 79.2 | E
Chevy Chase/Mariposa | SSSC | 6.0 | A | 6.3 | A
Chevy Chase/Boynton | Signalized | 16.5 | B | 19.1 | B
Chevy Chase/La Boice | SSSC | 12.3 | B | 21.1 | C
Chevy Chase/Adams | Signalized | 14.3 | B | 16.0 | B
Chevy Chase/Tyler/Acacia | Signalized | 44.5 | D | 45.0 | D
Notes: For signalized intersections, average intersection delay is reported in seconds per vehicle for all approaches. For side-street stop-controlled intersections, the delay and LOS for the most delayed individual movement is shown. All results are rounded to the nearest second. Source: Fehr & Peers, 2014 |  |  |  |  | 

## Slide 14: TRAVEL TIME STUDY
 | Peak Hour Travel Time Comparison |  |  |  |  |  | 
Location | Peak Hour | Eastbound (Min) |  |  | Westbound (Min) |  | 
 |  | Existing | With Lane reduction | Travel Time % Increase | Existing | With Lane reduction | Travel Time % Increase
Chevy Chase | AM | 2.4 | 3.4 | 42% | 2.7 | 3.8 | 41%
 | PM | 2.3 | 3.2 | 39% | 1.7 | 3.2 | 88%

## Slide 15
COMPUTER MODEL SIMULATION (SIMTRAFFIC)
  East Segment Existing AM Peak
  Ex East AM.wmv
  East Segment with Lane Reduction AM Peak
  Ln Red East AM.wmv
  West Segment Existing PM Peak
  Ex West PM.wmv
  West Segment with Lane Reduction PM Peak
  Ln Red West PM.wmv